## Slide 1: 面向大数据处理的内存系统
崔立骁

## Slide 2: 概述
内存墙问题（Memory Wall）
Memory Hierarchy
AMAT(Average Memory Access Time)
Cache & Cache Optimizations
C-AMAT(Concurrent-AMAT)
Layered Performance Matching

## Slide 3: 大数据时代

## Slide 4: 大数据时代(cont.)
计算密集型负载 数据密集型负载
I/O成为数据处理的瓶颈
内存也是数据处理的瓶颈
  内存墙问题
图片来源：舒继武教授ppt

## Slide 5: 内存墙问题
处理器性能快速提升
  单核处理器2004年增长约52%
  多核处理器每年增长约60%
内存性能增长缓慢
  每年增长约9%
内存与处理器之间的速度
差距不断变大
图源：计算机体系结构：量化研究方法

## Slide 7: Memory Hierarchy Introduction
• Programmers want unlimited amounts of memory with low latency
• Fast memory technology is more expensive per bit than slower memory
• Solution: organize memory system into a hierarchy
– Entire addressable memory space available in largest,
slowest memory
– Incrementally smaller and faster memories, each containing
a subset of the memory below it, proceed in steps up toward
the processor
• Temporal and spatial locality insures that nearly all
references can be found in smaller memories

## Slide 8: 多核处理器带来更严重的内存墙问题
Memory hierarchy design becomes more crucial with recent multi-core processors:
– Aggregate peak bandwidth grows with # cores:
• Intel Core i7 can generate two references per core per
clock
• Four cores and 3.2 GHz clock
25.6 billion 64-bit data references/second +
12.8 billion 128-bit instruction references
= 409.6 GB/s!
• DRAM bandwidth is only 6% of this (25 GB/s)
• Requires:
– Two levels of cache per core
– Shared third-level cache on chip

## Slide 9: 现代内存层次
- 用最廉价的技术向用户提供尽可能多的内存
- 用最快的技术提供尽可能好的访问性能。
图片来源：龙星计划

## Slide 10: Memory Technology Metrics
• Memory access latencies impact how quickly the information is available to the processor
– 100s of ps (CPU registers) to 10s… 100s of ns (main memory) for primary storage
• Memory bandwidth defines the maximum rate at which information is available for processing, preventing processor starvation
– 10s of GB/s for registers and L1 cache, single GB/s for main memory
• Capacity: determines maximum problem size possible to compute
– Capacities range from few bytes per register, few of KB to tens of MB for CPU caches, 100sof GB to 1 TB for hard disks
• Capacity density: determines additional costs associated with assembling storage of required capacity.

## Slide 11: 内存层次带来的改进
图片来源：龙星计划

## Slide 12: cache
Cache – Originally referring to the first level of the memory hierarchy – The principle of locality applies to many levels
Hit: data appears in some block in the upper level – Hit Rate: the fraction of memory accesses found in the upper level – Hit Time: Time to access the upper level , which consists of RAM access time + Time to determine hit/miss

## Slide 13: cache(cont.)
Miss: data needs to be retrieve from a block in the lower level (Block Y) – Miss Rate = 1 - (Hit Rate) – Miss Penalty: Time to replace a block in the upper level + Time to deliver the block the processor
Hit Time << Miss Penalty
图源：龙星计划

## Slide 14: cache(cont.)
Causes of misses – Compulsory First reference to a block – Capacity Blocks discarded and later retrieved – Conflict Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
Coherence Misses: – in multiprocessor systems and multi-core processors – Sometimes are false sharing

## Slide 15: AMAT(Average Memory Access Time)
AMAT = HitCycle + MR×AMP MR is the miss rate of cache accesses; and AMP is the average miss penalty
AMAT is Recursive - AMAT = HitCycle + MR×AMAT2 = HitCycle + MR×(H2 + MR2×AMP2)
-AMAT = HitCycle + MR×(H2 + MR2× AMAT3 ) = HitCycle + MR×(H2 + MR2×(H3 + MR3×AMP3))
-Etc

## Slide 16: 内存层次的性能优化表现
First-level
cache
Third
level
cache
main memory
Second
level
cache
1 clk
10 clk
20 clk
300 clk
– Miss rate: L1=10%, L2=5%, L3=1% (Be careful miss rate definition)
AMAT = 1 + 1 + 0.1 + 0.015
= 2.115
2.115 vs. 31 (if no L2, L3 memory hierarchy)

## Slide 17: Cache optimizations
Six basic cache optimizations:

## Slide 18: Cache Optimizations(cont.)
Advanced Optimizations
图源：计算机体系结构:量化研究方法(第五版)

## Slide 19: Cache Optimizations(cont.)
Memory Concurrency
  Pipelining Cache
  Nonblocking Cache
  Multi-banked Cache
  Prefetching (hardware and software)
  ……
L1
L2
…

## Slide 20: Memory Hierarchy & Parallelism
图源：龙星计划

## Slide 21: C-AMAT(Concurrent-AMAT)
The traditional AMAT(Average Memory Access Time) : AMAT = HitCycle + MR×AMP
MR is the miss rate of cache accesses; and AMP is the average miss penalty
Concurrent-AMAT (C-AMAT): C-AMAT = HitCycle/CH+ pMR×pAMP/CM
CH hit concurrency ; pure miss concurrency
pMR and pAMP are pure miss rate and average pure miss penalty
X.-H. Sun and D. Wang, "Concurrent Average Memory Access Time", in IEEE Computers, vol. 47, no. 5, pp. 74-80,May 2014.(IIT Technical Report,IIT/CS-SCS-2012-05)

## Slide 22: C-AMAT(cont.)
孙贤和，“C-AMAT：大数据时代的数据存取模型”，中国计算机学会通讯，2014年6月第6期
Miss is not important
Pure miss is important

## Slide 23: C-AMAT is Recursive
AMAT1 = HitCycle1 + MR1×AMAT2
Where AMAT2 = (HitCycle2 + MR2×AMP2)
X.-H. Sun, “Concurrent-AMAT: a mathematical model for Big Data access,” HPC-Magazine, May 12, 2014

## Slide 24: Physical meaning of κ in C − AMAT
Miss cycle = 14
Pure miss cycle = 6
Κ=6/14
图源：龙星计划

## Slide 25: The meaning of C-AMAT
First-level
cache
Third
level
cache
main memory
Second
level
cache
1 clk
10 clk
20 clk
300 clk
Hit Concurrency 2
3
4
6
AMAT=2.115

## Slide 26: The meaning of C-AMAT(cont.)
C-AMAT is an extension of AMAT to consider concurrency
  The same as AMAT, if no concurrency present
C-AMAT introduces the Pure Miss concept
  Only pure miss causes performance penalty
High locality may hurt performance
  High locality may lead to pure miss
Two contributions of concurrency
  Increase bandwidth
  Latency hiding (overlapping)

## Slide 27: The meaning of C-AMAT(cont.)
  Optimal ≠ Optimal Locality + Optimal Concurrence
  Balance locality, concurrency and Overlapping with CAMAT

## Slide 28: APC(access per cycle)
APC is measured as the number of memory accesses per cycle
  Each memory level has its own APC value
Benefits of APC
  Separate memory evaluation from CPU evaluation
  A better understanding of memory system as a whole
APC is measured as the number of memory accesses per memory active cycle or Access Per Memory Active Cycle

## Slide 29: APC(access per cycle)
APC = A/T
Measure T based on memory (active) cycle
  Can be measured for each layer of a memory hierarchy
Measure A based on the overlapping mode
  When there are several memory accesses co-existing during the same clock cycle, T only increases by one
C-AMAT = 1/APC

## Slide 30: Application: Layered Performance Matching
图源：龙星计划

## Slide 31: Match the Request with Supply
Match at each memory layer
Adjust the supply performance with concurrency

## Slide 32: C-AMAT in Action
C-AMAT = HitCycle/CH+ pMR×pAMP/CM
C-AMAT=1/APC
（1）
（2）
（3）
Y. Liu and X.-H. Sun, "Reevaluating Data Stall Time with the Consideration of Data
Access Concurrency," Journal of Computer Science and Technology (JCST), March, 2015

## Slide 33: A Example

## Slide 34: Sluice Gate Theory(存储闸门理论)
X.-H. Sun and Y.-H. Liu, "Utilizing Concurrency Data Access: A New Theory," in
Proc. of LCPC2016 (position paper), Sept, 2016, New York, USA

## Slide 35: Match approaches
增加访存的并发度
降低pure miss rate
降低pure miss penalty
……
具体实现
  Hardware technology
  Compiler technology
  Application algorithm technology

## Slide 36: Optimization Technique

## Slide 37: Sluice Gate Theory(存储闸门理论)
It’s possible to reduce stall time from 60% to 1%!
Maybe we can solve memory wall problem!!

## Slide 38
Thanks for your time! Questions & Answers